“SAFETY INSTRUCTION”

WARNING: To reduce the risk of serious injury, read the following safety instructions before using the Climber.

1. Read all warnings posted on the equipment

2. Read this Owner's Manual and follow it carefully before using the equipment. Make sure that it is properly assembled and tightened before use

3. We recommend that two people be available for assembly of this product

4. Keep children and pets away from the equipment. Do not allow children and pets to use or play on the equipment .Always keep children and pets away from the equipment when it is in use

5. It is recommended that you place this exercise equipment on an equipment mat

6. Set up and operate the equipment on a solid level surface. Do not position the equipment on loose rugs or uneven surfaces

7. Inspect the equipment for worn or loose components prior to each use

8. Tighten / replace any loose or worn components prior to using the equipment

9. Consult a physician prior to commencing an exercise program. If, at any time during exercise, you feel faint, dizzy, or experience pain, stop and consult your physician

10. Follow your physician's recommendations in developing your own personal fitness program

11. Always choose the workout which best fits your physical strength and flexibility level. Know your limits and train within them. Always use common sense when exercising

12. Before using this product, please consult your personal physician for a complete physical examination.

13. Do not wear loose or dangling clothing while using the equipment

14. Never exercise in bare feet or socks; always wear correct footwear, such as running, walking, or cross-training shoes

15. Be careful to maintain your balance while using, mounting, dismounting, or assembling the equipment loss of balance may result in a fall and serious bodily injury

16. Keep both feet firmly and securely on the Foot Pedals while exercising

17. The equipment should not be used by persons weighing over 300 pounds /136 kgs

18. The equipment should be used by only one person at a time

19. The equipment is for semi-commercial, light-commercial and home usage

20. Maintenance: Replace the defective components immediately and / or keep the equipment out of use until repair the equipment completely.

21. Make sure that adequate space is available for access to and passage around the equipment; keep at least a distance of 1 meter from any obstruction object while using the machine

WARNING: Before starting any exercise or conditioning program you should consult with your personal physician to see if you require a complete physical exam. This is especially important if you are over the age of 35, have never exercised before, are pregnant, or suffer from any illness

READ AND FOLLOW THE SAFETY PRECAUTIONS. FAILURE TO FOLLOW THESE       INSTRUCTIONS CAN RESULT IN SERIOUS BODILY INJURY

“ASSEMBLY PARTS”

Unpack the box in a clear area. Follow the List of Assembly Parts below to check and make sure all assembly parts are present and in good condition. Do not dispose of the packing material until the assembly process is completed. Assembly tools and hardware kit have included for you to use when assembling the product

| Console Upper Cover | Console Bottom Cover | Console Sleeve | Upright Post Assembly |
| --- | --- | --- | --- |
| Fixed Handlebar | Upper Handlebar | Pedal | Sliding Rail |
| Upright & Handlebar Sleeve | Nut & Leveler | Front & Rear Stabilizer | Main Frame Assembly |
| Linkage Plug | Rail Sleeve | Securing Cap | Pedal Support Arm |
| Handrail Base Cover | Pedal Bottom Case | Adaptor |  |

“HARDWARE IDENTIFICATION CHART”

Unpack the box in a clear area. Follow the List of Hardware Kit below. This chart is provided to help identify the hardware used in the assembly process. Place the washers, the end of bolts, or screws on the circles to check for the correct diameter. Use the small scale to check the length of the bolts and screws. Do not dispose of the packing material until the assembly process is completed

NOTICE: The length of all bolts and screws except those with flat heads is

measured from below the head to the end of the bolt or screw. Flat head

bolts and screws are measured from the top of the head to the end of the

bolt or screw

| After unpacking the unit, you will notice that the package includes 3 bags of hardware (HARDWARE KIT A, HARDWARE KIT B and HARDWARE KIT C). Assembly’s Step 1, 2, 3, 7, 8: Using HARDWARE KIT A Assembly’s Step 9, 10, 11: Using HARDWARE KIT B Note: Please review below to know the content of each hardware kit (A and B) Some small parts may have been pre-attached for shipping. If a part is not in the hardware bag, check to see if it has been pre-assembled |
| --- |
| HARDWARE KIT A | Part No. and Description | Q’TY |
|  | 79 Lock Washer (M8) | 6 pcs |
|  | 80 Washer (8x16x2.0t) | 2 pcs |
|  | 93 Bolt (M6xp1.0x25mm) | 2 pcs |
|  | 94 Bolt (M8xp1.25x16mm) | 4 pcs |
|  | 101 Bolt (M8xp1.25x90mm) | 2 pcs |
|  | 106 Bolt (M8xp1.25x90mm) | 2 pcs |
|  | 109 Carriage Bolt (M8xp1.25x90mm) | 2 pcs |
| HARDWARE KIT A | Part No. and Description | Q’TY |
|  | 112 Nylon Nut (M8xp1.25) | 4 pcs |
|  | 131 Self-Tapping Screw, Flat Head (M4x10mm) | 6 pcs |
| HARDWARE KIT B | Part No. and Description | Q’TY |
|  | 79 Lock Washer (M8) | 1 pcs |
|  | 80 Washer (8x16x2.0t) | 1 pcs |
|  | 88 Self-Tapping Screw, Flat Head (M4x16mm) | 4 pcs |
|  | 90 Bolt (M5xp0.8x25mm) | 4 pcs |
|  | 91 Bolt (M5xp0.8x15mm) | 4 pcs |
|  | 98 Bolt (M6xp1.0x15mm) | 4 pcs |
|  | 99 Bolt (M6xp1.0x35mm) 100 Bolt (M8xp1.25x45mm) | 4 pcs 1 pcs |
|  | 110 Nylon Nut (M6xp1.0) | 4 pcs |

“BEFORE YOU BEGIN”

| Thank you for choosing the Climber. We take great pride in producing this quality product and hope it will provide many hours of quality exercise to make you feel better, look better and enjoy life to its fullest. Yes, it's a proven fact that a regular exercise program can improve your physical and mental health. | Too often, our busy lifestyles limit our time and opportunity to exercise. The equipment provides a convenient and simple method to begin your assault on getting your body in shape and achieving a happier and healthier lifestyle. Before reading further, please review the drawing below and familiarize yourself with the parts that are labeled. Read this manual carefully before using the equipment. |
| --- | --- |

THE FOLLOWING TOOLS ARE INCLUDED FOR ASSEMBLY:

“ASSEMBLE INSTRUCTIONS”

STEP 1 – Front Stabilizer Assembly

- Attach the Front Stabilizer (2) to the Main Frame (1).

- Fully secure two Washers (8x16x2.0t)(80), two Lock Washers (M8)(79) and two Bolts (M8xp1.25x90mm)(101) that attach to the Front Stabilizer (2) to the Main Frame (1).

STEP 2 – Sliding Rail Assembly

NOTE: For shipping purpose, 1pcs Washer (8x16x2.0t)(80), 1pcs Lock Washer (M8)(79) and 1pcs Bolt (M8xp1.25x20mm)(103) are attached on the Main Frame (1) as the draft shown on the left.

- Remove 1pcs Washer (8x16x2.0t)(80), 1pcs Lock Washer (M8)(79) and 1pcs Bolt (M8xp1.25x20mm)(103) from the Main Frame (1).

- Attach the Left Sliding Rail (4) to the Main Frame (1) by securing with 1pcs Washer (8x16x2.0t)(80), 1pcs Lock Washer (M8)(79) and 1pcs Bolt (M8xp1.25x20mm)(103). For letting the sliding rail assembly attaches nicely to the rear stabilizer, please on this step b., do not fully tighten washer and bolts (79, 80 and 103).

- Then attach the Securing Cap (30) and secure with 1pcs Bolt (M6xp1.0x25mm)(93).

- Repeat the above same procedure for the right side.

STEP 3 – Rail Sleeve & Rear Stabilizer Assembly

- Attach the Rail Sleeve (31) to the Rear Stabilizer (3).

NOTE: For shipping purpose, 2pcs Washers (8x16x2.0t)(80), 2pcs Lock Washers (M8)(79) and 2pcs Bolts (M8xp1.25x20mm)(103) are attached to the back of the Rear Stabilizer (3) as the draft shown on the right.

- Remove 2pcs Washers (8x16x2.0t)(80), 2pcs Lock Washers (M8)(79) and 2pcs Bolts (M8xp1.25x20mm)(103) from the back of the Rear Stabilizer (3).

- Attach the Rear Stabilizer (3) to the Main Frame (1) and then go on to attach the Left and Right Sliding Rail (4,5) to the Rear Stabilizer (3).

- Follow the drawing line to secure with 2pcs Washers (8x16x2.0t)(80), 2pcs Lock Washers (M8)(79), 2pcs Bolts (M8xp1.25x20mm)(103), 2pcs Carriage Bolt (M8xp1.25x90mm)(109) and 2pcs Nylon Nuts (M8xp1.25)(112).

- Go back to Step 2 to fully tighten 2pcs Washers (8x16x2.0t)(80), 2pcs Lock Washers (M8)(79) and 2pcs Bolts (M8xp1.25x20mm)(103) on two upper sides of the sliding rail.

- Attach the Leveler (23) and Nut (M8xp1.25)(114) to the middle of the Main Frame’s base (1). Adjust the Leveler (23) until it meets the base of the Main Frame. Then tighten the Nut (114) securely against the Main Frame (1). NOTE: The purpose of adjust the Leveler (23) is to level the item and get more support for the base on the Main Frame. Adjust the Leveler (23) until the item sets on the floor without rocking

“ASSEMBLE INSTRUCTIONS”

STEP 4 – Upright Sleeve & Upright Post Assembly

- Slide the Upright Sleeve (37) onto the Upright Post (6).

NOTE: For shipping purpose, 5pcs Nylon Nuts (M8xp1.25)(112) are attached on the Main Frame (1) as the draft shown on the right.

- Remove 5pcs Nylon Nuts (M8xp1.25)(112) from the Main Frame (1).

- Refer to FIG.A’s 3 following drawings, in order to let point A (Middle Handlebar) and point B (Pedal Arm Connector) could connect nicely, before attaching the Upright Post (6) to the Main Frame (1), make sure raising point A (Middle Handlebar) in 45 degree, then attach the Upright Post (6) to the Main Frame (1) and secure with 5pcs Nylon Nuts (M8xp1.25)(112). **Please don’t fully tighten nuts (112), wait until Step 6 to fully tighten the nuts.**

STEP 5 – Connection Wire Assembly

Connect the Middle Connection Wire (118) to the Lower Connection Wire (119). NOTE: Be careful not to pinch the wires.

STEP 6 – Linkage & Linkage Plug Assembly

NOTE: For shipping purpose, 1pcs Bolt (M8xp1.25x50mm)(104), 1pcs Nylon Nut (M8xp1.25)(112) and 1pcs Bolt (M5xp0.8x25mm)(92) are attached to the P	edal Arm Connector (16) as the draft shown on the right.

- Remove 1pcs Bolt (M8xp1.25x50mm)(104), 1pcs Nylon Nut (M8xp1.25)(112) and 1pcs Bolt (M5xp0.8x25mm)(92) from the P	edal Arm Connector (16).

- Follow the FIG 1 to attach the Right Linkage (15) to the Right Pedal Arm Connector (16) by securing with 1pcs Bolt (M8xp1.25x50mm)(104), 1pcs Nylon Nut (M8xp1.25)(112). NOTE: In order to let the Linkage (15) rotate smoothly, after fully tighten the Bolts (104) and Nuts (112), please loose the Nuts (112) just 1/8 counterclockwise turn.

- Attach the Right Linkage Plug (58) to the Right Pedal Arm Connector (16) and secure with 1pcs Bolt (M5xp0.8x25mm)(92).

- Repeat the above same procedure for the left side.

- Go back to Step 4 to fully tighten 5pcs Nylon Nuts (M8xp1.25)(112) on the bottom of the Upright Post (6).

- Slide the Upright Sleeve (37) down to cover the open area of the Main Frame (1).

“ASSEMBLE INSTRUCTIONS”

STEP 7 – Pedal Support Arm Assembly

- Refer to the inset drawing FIG .2, cut off the tie (A) on the front end of the Right Pedal Support Arm (14). NOTE: Please be sure that the Shaft Sleeve (68) inside the Pedal Support Arm (14) does not fall off while cutting off the tie.

- Attach the front end of the Right Pedal Support Arm Assembly (14) to the Right Pivoting Arm (12) with 1pcs Bolt (M8xp1.25x90mm)(106) and 1pcs Nut (M8xp1.25)(112) NOTE: Please be sure that Bolt (106) would slide through the Shaft Sleeve (68) inside front end of the Right Pedal Support Arm Assembly (14) during assembly.

NOTE: Refer to the inset drawing FIG.3, for shipping purpose, 1pcs Roller Spacer (56), 1pcs Bolt (M8xp1.25x65mm)(105), 1pcs Nylon Nut (M8xp1.25)(112) are attached to the Right Roller Bracket (69) as the draft shown on the right.

- Remove 1pcs Roller Spacer (56), 1pcs Bolt (M8xp1.25x65mm)(105), 1pcs Nylon Nut (M8xp1.25)(112) from the Right Roller Bracket (69).

- Refer to FIG 3. Place the roller under the Right Pedal Support Arm (14) onto the Right Sliding Rail (5).

- Then place the Roller Spacer (56) under the Right Sliding Rail (5), secure 1pcs Bolt (M8xp1.25x65mm)(105) through the Roller Spacer (56) with 1pcs Nylon Nut (M8xp1.25)(112). NOTE: Please be sure not to over-tighten Bolt (105) and Nut (112), after tightening, make sure the Roller Spacer (56) could still rotate nicely by using finger to rotate the Roller Spacer (56). If the Roller Spacer (56) is unable to rotate, would cause the roller couldn’t slide smoothly on the Sliding Rail.

- Repeat the above same procedure for the left side.

STEP 8 – Pedal Assembly

- Attach the Pedal Bottom Case(130) to the Right Pedal (54) and secure with 3pcs Self-Tapping Screw, Flat Head (M4x10mm) (131).

- Attach the Right Pedal (54) to the upper Pedal Plate located on the rear of the Right Pedal Support Arm (14) and secure with 2pcs Lock Washers (M8)(79) and 2 pcs Bolts (M8xp1.25x16mm)(94).

- Repeat the above same procedure for the left side.

“ASSEMBLE INSTRUCTIONS”

STEP 9 – Handrail Base Cover Assembly

To assemble the Handrail Base Cover (128, 129), place the Left Handrail Base Cover (128) at the inner side of the Right Middle Handlebar (11). Place the Right Handrail Base Cover (129) at the outer side of the Right Middle Handlebar (11). Bolt the Handrail Base Cover (128, 129) with 2pcs Self-Tapping Screws, Flat Head (M4x16mm)(88). Repeat the above assembly process on the left side.

STEP 10 – Fixed Handlebar Assembly

NOTE: 4pcs Washers (8x16x2.0t)(80), 4pcs Lock Washers (M8)(79) and 4pcs Bolts (M8xp1.25x16mm)(102) will already be attached on two sides of the Fixed Handlebar (7).

- Remove 4pcs Washers (8x16x2.0t)(80), 4pcs Lock Washers (M8)(79) and 4pcs Bolts (M8xp1.25x16mm)(102) from the Fixed Handlebar (7).

- Position the Fixed Handlebar (7) in place through the Upright Post Assembly (6) and secure with 5pcs Washers (8x16x2.0t)(80), 5pcs Lock Washers (M8)(79) and 4pcs Bolts (M8xp1.25x16mm)(102)and 1pcs Bolt (M8xp1.25x45mm)(100) NOTE: 1pcs Washer (8x16x2.0t)(80), 1pcs Lock Washer (M8)(79), 1pcs Bolt (M8xp1.25x45mm)(100) will be packed into HARDWARE KIT B.

STEP 11 – Console and Connection Wire Assembly

- Follow FIG.4 to attach the Console Bottom Cover (33) to the Console (32) and secure with 4pcs Bolts (M5xp0.8x25mm)(90).

- Place and secure the Console Assembly (32, 33) onto the iron plate of the Upright Post Assembly (6) using 4pcs Bolts (M6xp1.0x15mm)(98).

- Connect the Front Connection Wire (117) to the Middle Connection Wire (118). Be care not to pinch the wires

- Connect the Front Pulse Sensor Wire (124) to the Rear Pulse Sensor Wire (125). Be care not to pinch the wires

“ASSEMBLE INSTRUCTIONS”

STEP 12 – Console Sleeve, Handlebar Sleeve & Upper Handlebar Assembly

- Attach the Right Console Sleeve (35) and the Left Console Sleeve (34) to the Upright Post Assembly (6). Bolt the Console Sleeve (34, 35) with 4pcs Bolts (M5xp0.8x15mm)(91).

NOTE: Make sure that the Right Console Sleeve (35) and the Left Console Sleeve (34) would cover the Upright Cover and the lowest layer of the Console Bottom Cover (33) as the following illustration shown.

- Slide the Right Handlebar Sleeve (44) onto the Right Upper Handlebar (9).

- Attach the Right Upper Handlebar (9) onto the Right Middle Handlebar (11) and secure with 2 Bolts (M6xp1.0x35mm)(99) and 2pcs Nylon Nuts (M6xp1.0)(110).

- Slide the Right Handlebar Sleeve (44) down until it touches the middle part of Handlebar.

- Repeat the above same procedure for the left side.

- Finish the assembly, make sure that all parts are tightened before you use the equipment.

STEP 13 – AC Adaptor

- Connect the Adaptor to the connector located on the front side of the Main Frame (1).

- Plug the Adaptor into an electrical outlet to light up the console.

“OPERATION INSTRUCTIONS”

HOW TO ADJUST THE ADJUSTING ENDCAPS OF THE REAR STABILIZER

- After placing the equipment in the intended location for use, check the stability of the equipment

- If it’s the one of the Adjusting EndCaps (27) on rear end of the Rear Stabilizer (3) causes a slight rocking motion. To level the equipment, turn one or both of the Adjusting EndCaps (27) in clockwise or counter-clockwise direction until the equipment sets on the floor without rocking

HOW TO ADJUST CONSOLE ANGLE

To get the best console angle, it’s suggested to use both hands to hold the upper and lower end of the console and gently adjust the console angle to the proper position

HOW TO TOW THE ITEM SAFELY

Hold the Rear Stabilizer (3) up with two hands and tow the item to the desired place carefully

- Make sure the floor is level while towing the item

HOW TO ADJUST THE STAND ON THE MIDDLE OF MAIN FRAME’S BASE

NOTE: The purpose of adjust the Leveler (23) is to level the item and get more support for the base on the Main Frame. After finishing all assembly process, place the item on a flat surface. Adjust the Leveler (23) until the item sets on the floor without rocking, then tighten the Nut (114) securely against the Main Frame (1).

“OPERATION INSTRUCTIONS”

HOW TO ADJUST THE STRIDE LENGTH

The Climber is quipped with four adjustable stride lengths from 19’’ (483mm) to 22’’ (539mm)

- To adjust the stride length, loosen and pull the Spring Knob (48). Move the Pivoting Arm (12) to the proper desired position

- Release the Spring Knob (48) and make sure the pin on the knob get into the adjustment hole in the Pivoting Arm (12).

- Repeat the above process to adjust the stride length on left side

NOTE:

1. Always adjust the Right & Left Pivoting Arm (12) in the same height.

2. Securely tighten Right & Left Spring Knob (48) before exercising

“CONSOLE INSTRUCTIONS”

Power ON

- Make sure the item’s adaptor is correctly plugged into the socket

- Pedaling or pressing any keys to active the console. The console display will then light up with a short beep sound, indicating the console will be ready for use

Power Off

The console would automatically shut off after 4 minutes of inactivity

Program List

| P1 MANUAL PROGRAM | P2 ROLLING PROGRAM | P3 VALLEY PROGRAM | P4 FAT BURN PROGRAM |
| --- | --- | --- | --- |
| P5 RAMP PROGRAM | P6 FITNESS TEST PROGRAM | P7 RANDOM PROGRAM | P8 BODY FAT PROGRAM |
| P9 TARGET H.R. PROGRAM | P10 60% H.R.C. PROGRAM | P11 75% H.R.C. PROGRAM | P12 85% H.R.C. PROGRAM |
| P13 USER 1 MODE PROGRAM | P14 USER 2 MODE PROGRAM | P15 USER 3 MODE PROGRAM | P16 USER 4 MODE PROGRAM |

“CONSOLE INSTRUCTIONS – CONSOLE BUTTONS ”

Console Buttons

|  | Press START/PAUSE to begin your exercise Press START/PAUSE again to stop and pause all functions during your exercise program. All the date on the display will then freeze. Press START/PAUSE again to resume the program and all the date displayed will continue until the program has finished. HOLD TO RESET function: Continue pressing START/PAUSE, all the date will return to 0 and the console will return to POWER ON status |
| --- | --- |
|  | Press ENTER to confirm the program function (PROGRAM, TIME, HEIGHT, WEIGHT, DISTANCE, CALORIES, AGE, GENDER, TARGET H.R. and TORQUE/RESISTANCE LEVEL in each time interval) |
|  | Press UP to increase the values of the program function (PROGRAM, TIME, HEIGHT, WEIGHT, DISTANCE, CALORIES, AGE, GENDER, TARGET H.R. and TORQUE/RESISTANCE LEVEL in each time interval) |
|  | Press DOWN to decrease the values of the program function (PROGRAM, TIME, HEIGHT, WEIGHT, DISTANCE, CALORIES, AGE, GENDER, TARGET H.R. and TORQUE/RESISTANCE LEVEL in each time interval) |

“CONSOLE INSTRUCTIONS – CONSOLE BUTTONS ”

|  | During workout (after pressing START/PAUSE), the user could press MODE to select SPEED, DISTANCE and CALORIES, or RPM, ODO (Odometer) and WATT RPM, ODO, WATT will show at the same time SPEED, DISTANCE, CAL. will show at the same time DISTANCE and ODO (ODOMETER) information: DISTANCE: This measures the total distance from 0 to 999 km/Mile. After pressing START/PAUSE, DISTANCE will count up. Press START/PAUSE again to pause all functions and DISTANCE value during your exercise program. Press START/PAUSE again to resume the program and DISTANCE value will continue counting up until the program finish The console would automatically shut off after 4 minutes of inactivity. The DISTANCE value’s counting will restart from zero after pedaling or pressing any keys to active the console again ODO (ODOMETER): The function of ODO and DISTANCE are similar will accumulate the total distance traveled by the item during workout. If there is any necessary to reset ODO’s distance value, press UP, MODE, DOWN and ENTER at the same time to let the motor automatically calibrate to reset ODO value to zero |
| --- | --- |
|  | PULSE RECOVERY button measures how quickly you return to a resting hear rate after exercising. You could use this button to measure improvement as you get into shape The console will monitor your pulse for 60 seconds and calculate a HEART RATE RECOVERY value from F1.0 to F6.0. F1.0 is best; F6.0 is worst (For Reference Only) The readout should only be used as a comparison between workouts. It’s recommended to use right after any aerobic exercise. Stop exercising before starting the function. Your pulse will be displayed approximately few seconds after the heart symbol “” is displayed NOTE: If you don’t hold the HEART RATE SENSORS on the handrails with both hands properly, the console’s HEART RATE value would show “0” and the main screen would show “F6.0” after the console counts down to zero, which means the HEART RATE SENSORS won’t be able to pick up the signals. Press any keys to stop the long beep sound, then press PULSE RECOVERY button again and make sure to hold the HEART RATE SENSORS on the handrails with both hands properly this time. |

“CONSOLE INSTRUCTIONS”– CONSOLE FUNCTIONS”

Console Functions

|  | PROGRAM: The console comes with 16 preset programs Displays programs for selection during setup, from P1 ~ P16 Displays the selected program during exercise LEVEL: Displays torque/resistance level of the current program, from 1 to 16 torque/resistance level; 1 level increment |
| --- | --- |
|  | TIME: Count Up: If a target time was not selected, TIME will count up from 0:00 to maximum 99:59 minutes Count Down: If you have set the target time, the console will count down from that selected target time down to 0:00 HEIGHT: Display range: 110 ~ 250cm; 0.5 cm increment / 3’08’’ ~ 8’ 00’’; 1 inch increment; the product is not recommended for children’s use WEIGHT: Display range: 10 ~ 200KG; 0.2 KG increment / 23 ~ 440 LBS; 0.5 LBS increment; the product is not recommended for children’s use |
|  | DISTANCE: Count Up: If a target distance was not selected, this would measure the total distance from 0:00 to 999 km/mile Count Down: If you have set the target distance, the console will count down from that selected target distance down to 0 During workout (after pressing START/PAUSE), the user could press MODE button to select DISTANCE, or ODO (Odometer) |
|  | ODO: The function of ODO and DISTANCE are similar will accumulate the total distance traveled by the item during workout DIFFERENT RESET INFO. of DISTANCE & ODO: RESET INFO. of DISTANCE: The console would automatically shut off after 4 minutes of inactivity. The DISTANCE value’s counting will restart to zero after pedaling or pressing any keys to active the console again RESET INFO. of ODO: To reset ODO’s distance value, press UP, MODE, DOWN and ENTER at the same time to let the motor automatically calibrate to reset ODO value to zero FAT%: During BODY FAT TEST, the result would display the percentage of body fat in BODY FAT PROGRAM (P8) Your body fat percentage is simply the percentage of the fat your body contains |

“CONSOLE INSTRUCTIONS”– CONSOLE FUNCTIONS”

|  | CALORIES: Count Up: If target calories were not selected, this measures total calories your body burned during exercise Count Down: If you have set the preference value of calories, the console will count down from that selected target calories down to 0 BMR: During BODY FAT TEST, the result would display the value of BMR in BODY FAT PROGRAM (P8) BMR (BASAL METABOLIC RATE) is a rate at which the body burns calories to maintain normal body functions while at rest WATT: Display the current value of Watt during exercise |
| --- | --- |
|  | TARGET H.R.: Display range: 60 ~ 220 BPM (beats per minute) ; 1 BPM increment AGE: Display range: 10 ~ 99 years old; 1 year-old increment NOTE: Although the console allows input for age beginning at 10 years old, the product is not recommended for children’s use BMI: During BODY FAT TEST, the result would display the value of BMI in BODY FAT PROGRAM (P8) BMI (BODY MASS INDEX) is a height/weight formula. From the value of your BMI, you can see whether you are underweight, normal weight, overweight or obese |
|  | HEART RATE: You must place both of your hands on the Pulse Sensors on the Handlebar. Your pulse will be displayed approximately few seconds after the heart symbol “” is displayed If you do not place your hands correctly and a few seconds passes without a pulse input, the console will turn off the pulse circuit. Place your hands back on the Pulse Sensors correctly, the pulse readout will appear again BODY TYPE: During BODY FAT TEST, the result would display the value of BODY TYPE in BODY FAT PROGRAM (P8) |

“CONSOLE INSTRUCTIONS – MANUAL PROGRAM (P1)”

“1” Prior information: Press any button on the console or begin pedaling to turn on the console

- Make sure that the power cord is properly plugged into the socket.

- The console would automatically shut off after 4 minutes of inactivity

- Press any button on the console or begin pedaling to turn on the console. After a few seconds, the console will then light up with a short beep sound, indicating the console will be ready for use

“2” Prior information: ”HOLD TO RESET” button, an easy way to reset and enter into POWER ON status

Continue pressing START/PAUSE a few seconds, all the date will reset to the initial value and the console will return to POWER ON status

“3” Normal way to operate MANUAL PROGRAM (P1)

“A.“ENTER MANUAL PROGRAM (P1)”

“CONSOLE INSTRUCTIONS – MANUAL PROGRAM (P1)”

“B. SET THE DESIRED TIME or DESIRED DISTANCE

To avoid the user to select TIME and DISTANCE in the same program to confuse the user couldn’t distinguish which one (TIME or DISTANCE) as the first priority. User could only select TIME or DISTANCE in the same program, one at the time

| If you would like to select TIME value, not DISTANCE value: UP or DOWN button: After pressing the ENTER button to enter into MANUAL PROGRAM (P1), the TIME function mode will appear with the display flashing “0:00”. Use UP or DOWN buttons to set the desired TIME (1:00 TO 99:00; 1 MINUTE INCREMENT) NOTE for TIME: Count Up: If a target time was not selected, TIME will count up from 0:00 to maximum 99:59 minutes Count Down: If you have set the target time, the console will count down from that selected target time down to 0:00 | If you would like to select DISTANCE value, not TIME value: ENTER button and then UP or DOWN button: After pressing the ENTER button to enter into MANUAL PROGRAM (P1), the TIME function mode will appear with the display flashing “0:00”. Press the ENTER button again, the DISTANCE function mode will then appear with the display flashing “0.0” Use UP or DOWN buttons to set the desired DISTANCE (1 TO 999KM/MILE; 1 KM/MILE INCREMENT) NOTE for DISTANCE: Count Up: If a target distance was not selected, this would measure the total distance from 0:00 to 999 km/mile Count Down: If you have set the target distance, the console will count down from the selected target time down to 0 |
| --- | --- |

“CONSOLE INSTRUCTIONS – MANUAL PROGRAM (P1)”

“C. SET THE DESIRED CALORIES and YOUR AGE”

  - ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm TIME or DISTANCE value and enter the mode to set the

CALORIES

b. Use UP or DOWN buttons to set the desired CALORIES (10 TO 9990KCAL; 10 KCAL

INCREMENT)

NOTE for CALORIES:

- Count Up: If target calories was not selected, this would measure total calories burned during exercise

- Count Down: If you have set the preference value of calories, the console will count down from that selected value down to 0

  - ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm the CALORIES value and enter the mode to set the AGE

b. Use UP or DOWN buttons to set your AGE (10 TO 99 YEARS OLD; 1 YEAR OLD INCREMENT)

NOTE for AGE:

NOTE: Although the console allows input for ages beginning at 10 years old, the product is not recommended for children’s use

“D. START EXERCISE”

START/ PAUSE button: Press START/ PAUSE to begin exercise. “START” would then appear on the screen

“ E. DURING WORKOUT, ALWAYS MONITOR YOUR CURRENT HEART RATE STATUS”

NOTE for HEART RATE:

- You must place both of your hands on the Pulse Sensors located on the Seat Handlebar. Your pulse will be displayed approximately few seconds after the heart symbol “” is         displayed

- If you do not place your hands correctly and a few seconds pass without a pulse input, the console will turn off the pulse circuit. The console will then display an error message “P”. Place your hands back on the Pulse Sensors correctly, the pulse readout will appear again

“CONSOLE INSTRUCTIONS – MANUAL PROGRAM (P1)”

“F. DURING WORKOUT, THE TORQUE/TENSION LEVEL IS EASILY CHANGED AT ANY TIME”

UP or DOWN button: You can change the torque/tension level (from 1 to 16 levels) at any

time during workout by pressing UP or DOWN button

G. DURING WORKOUT, ALWAYS NOTICE TARGET HEART RATE – A EASY WAY TO SET A GOAL TO “STRENGTHEN YOUR CARDIOVASCULAR WORKOUT”

- To improve your cardiovascular condition, while input your personal age during the setting mode, the console will calculate the appropriate TARGET HEART RATE for you automatically

- The TARGET HEART RATE calculation is based on 85% of the maximum heart rate. For example: For a 30-year-old user, the max. user heart rate should be 161 = (220-30) x 85%

- The console will monitor your pulse and compare the value of your pulse with TARGET HEART RATE. The value of HEART RATE will keep flashing to warn you to slow down or lower the torque/resistance level if your pulse value is greater than TARGET HEART RATE

H. DURING WORKOUT, HOW TO REVIEW SPEED, DISTANCE, CALORIES, RPM, ODO (ODOMETER) AND WATT”

During workout (after pressing START/PAUSE), the user could press MODE to select SPEED, DISTANCE and CALORIES, or RPM, ODO (Odometer) and WATT

RPM, ODO, WATT will show at the same time   SPEED, DISTANCE, CAL. will show at the same time

About ODO (odometer), the function is similar to DISTANCE, will accumulate the total distance traveled by the item during workout. If there is any necessary to reset ODO’s distance value, press UP, MODE, DOWN and ENTER at the same time to let the motor automatically calibrate to reset ODO value to zero

“CONSOLE INSTRUCTIONS – PROGRAM (P2 ~ P7)”

“1” Prior information: Press any button on the console or begin pedaling to turn on the console

  - Make sure that the power cord is properly plugged into the socket

  - The console would automatically shut off after 4 minutes of inactivity

  - Press any button on the console or begin pedaling to turn on the console. After a few seconds, the console will then light up with a short beep sound, indicating the console will be ready for use

“2” Prior information: ”HOLD TO RESET” button, an easy way to reset and enter into POWER ON status

Continue pressing START/PAUSE a few seconds, all the date will reset to the initial value and the console will return to POWER ON status

“CONSOLE INSTRUCTIONS – PROGRAM (P2 ~ P7)”

“3” Normal way to operate PROGRAM (P2~P7)

“A.“ENTER MANUAL PROGRAM (P2~P7)”

- START/PAUSE button:

If you have selected other program (P1 or P8 ~ P16), pressing START/PAUSE button to pause the current program

- UP or DOWN button:

Press UP or DOWN button to select PROGRAM (P2 ~ P7)

- ENTER button:

Press ENTER button to confirm and enter PROGRAM (P2 ~ P7)

“B. SET THE DESIRED TIME or DESIRED DISTANCE

To avoid the user to select TIME and DISTANCE in the same program to confuse the user couldn’t distinguish which one (TIME or DISTANCE) as the first priority. User could only select TIME or DISTANCE in the same program, one at the time

| If you would like to select TIME value, not DISTANCE value: UP or DOWN button: After pressing the ENTER button to enter into PROGRAM (P2 ~ P7), the TIME function mode will appear with the display flashing “0:00” Use UP or DOWN buttons to set the desired TIME (1:00 TO 99:00; 1 MINUTE INCREMENT) NOTE for TIME: Count Up: If a target time was not selected, TIME will count up from 0:00 to maximum 99:59 minutes Count Down: If you have set the target time, the console will count down from that selected target time down to 0:00 | If you would like to select DISTANCE value, not TIME value: ENTER button and then UP or DOWN button: After pressing the ENTER button to enter into PROGRAM (P2 ~ P7), the TIME function mode will appear with the display flashing “0:00”. Press the ENTER button again, the DISTANCE function mode will then appear with the display flashing “0.0” Use UP or DOWN buttons to set the desired DISTANCE (1 TO 999KM/MILE; 1 KM/MILE INCREMENT) NOTE for DISTANCE: Count Up: If a target distance was not selected, this would measure the total distance from 0:00 to 999 km/mile Count Down: If you have set the target distance, the console will count down from the selected target time down to 0 |
| --- | --- |

“CONSOLE INSTRUCTIONS – PROGRAM (P2 ~ P7)”

“C. SET THE DESIRED CALORIES and YOUR AGE”

- ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm the TIME or DISTANCE value and enter the mode to set the CALORIES

b. Use UP or DOWN buttons to set the desired CALORIES (10 TO 9990KCAL; 10 KCAL

INCREMENT)

NOTE for CALORIES:

- Count Up: If target calories was not selected, this would measure total calories burned during exercise

- Count Down: If you have set the preference value of calories, the console will count down from that selected value down to 0

- ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm the CALORIES value and enter the mode to set the AGE

b. Use UP or DOWN buttons to set your AGE (10 TO 99 YEARS OLD; 1 YEAR OLD INCREMENT)

NOTE for CALORIES:

NOTE: Although the console allows input for ages beginning at 10 years old, the product is not recommended for children’s use

“D. START EXERCISE”

START/ PAUSE button: Press START/ PAUSE to begin exercise. “START” would then appear on the screen

“ E. DURING WORKOUT, ALWAYS MONITOR YOUR CURRENT HEART RATE STATUS”

NOTE for HEART RATE:

- You must place both of your hands on the Pulse Sensors located on the Seat Handlebar. Your pulse will be displayed approximately few seconds after the heart symbol “” is displayed

- If you do not place your hands correctly and a few seconds pass without a pulse input, the console will turn off the pulse circuit. The console will then display an error message “P”. Place your hands back on the Pulse Sensors correctly, the pulse readout will appear again

“CONSOLE INSTRUCTIONS – PROGRAM (P2 ~ P7)”

“F. DURING WORKOUT, THE TORQUE/TENSION LEVEL IS EASILY CHANGED AT ANY TIME”

UP or DOWN button: You can change the torque/tension level (from 1 to 16 levels) at any

time during workout by pressing UP or DOWN button

G. DURING WORKOUT, ALWAYS NOTICE TARGET HEART RATE – A EASY WAY TO SET A GOAL TO “STRENGTHEN YOUR CARDIOVASCULAR WORKOUT”

- To improve your cardiovascular condition, while input your personal age during the setting mode, the console will calculate the appropriate TARGET HEART RATE for you automatically

- The TARGET HEART RATE calculation is based on 85% of the maximum heart rate. For example: For a 30-year-old user, the max. user heart rate should be 161 = (220-30) x 85%

- The console will monitor your pulse and compare the value of your pulse with TARGET HEART RATE. The value of HEART RATE will keep flashing to warn you to slow down or lower the torque/resistance level if your pulse value is greater than TARGET HEART RATE

H. DURING WORKOUT, HOW TO REVIEW SPEED, DISTANCE, CALORIES, RPM, ODO (ODOMETER) AND WATT”

During workout (after pressing START/PAUSE), the user could press MODE to select SPEED, DISTANCE and CALORIES, or RPM, ODO (Odometer) and WATT

RPM, ODO, WATT will show at the same time   SPEED, DISTANCE, CAL. will show at the same time

About ODO (odometer), the function is similar to DISTANCE, will accumulate the total distance traveled by the item during workout. If there is any necessary to reset ODO’s distance value, press UP, MODE, DOWN and ENTER at the same time to let the motor automatically calibrate to reset ODO value to zero

“CONSOLE INSTRUCTIONS – BODY FAT PROGRAM (P8)”

“1” Prior information: Press any button on the console or begin pedaling to turn on the console

- Make sure that the power cord is properly plugged into the socket.

- The console would automatically shut off after 4 minutes of inactivity

- Press any button on the console or begin pedaling to turn on the console. After a few seconds, the console will then light up with a short beep sound, indicating the console will be ready for use

“2” Prior information: ”HOLD TO RESET” button, an easy way to reset and enter into POWER ON status

Continue pressing START/PAUSE a few seconds, all the date will reset to the initial value and the console will return to POWER ON status

“3” Normal way to select and operate BODY FAT PROGRAM (P8)

“A.“ENTER BODY FAT PROGRAM (P8)”

- START/PAUSE button:

If you have selected other program (P1 ~ P7, P9 ~ P16), pressing START/PAUSE button to pause the current program

- UP or DOWN button:

Press UP or DOWN button to select BODY FAT PROGRAM (P8)

- ENTER button:

Press ENTER button to confirm and enter BODY FAT PROGRAM (P8)

“CONSOLE INSTRUCTIONS – BODY FAT PROGRAM (P8)”

“B. SET THE PERSONAL INFO. ( GENDER, HEIGHT and AGE )”

    - UP or DOWN button:

After pressing the ENTER button, the GENDER function mode will appear with the display flashing “”. Use UP or DOWN buttons to set your GENDER

    - ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm your GENDER and enter the mode to set your HEIGHT

b. Use UP or DOWN buttons to set your HEIGHT (110 ~ 250CM; 0.5 CM INCREMENT /

3’08’’ ~ 8’ 00’’; 1 INCH INCREMENT)

NOTE for HEIGHT:

NOTE: The product is not recommended for children’s use

    - ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm your HEIGHT value and enter the mode to set your

WEIGHT

b. Use UP or DOWN buttons to set your WEIGHT (10 ~ 200KG; 0.2 KG INCREMENT / 23 ~

440 LBS; 0.5 LBS INCREMENT)

NOTE for WEIGHT:

NOTE: The product is not recommended for children’s use

    - ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm your WEIGHT value and enter the mode to set the

AGE

b. Use UP or DOWN buttons to set your AGE (10 TO 99 YEARS OLD; 1 YEAR OLD

INCREMENT)

NOTE for AGE:

NOTE: Although the console allows input for ages beginning at 10 years old, the product is not recommended for children’s use

“C. START TESTING YOUR BODY FAT”

START/ PAUSE button: Press START/ PAUSE to start testing your body fat. The testing time takes about 10 seconds, please review the next page to understand the meaning of the result

“CONSOLE INSTRUCTIONS – BODY FAT PROGRAM (P8)”

“D. THE BODY FAT RESULT INFORMATION”

- BMI (BODY MASS INDEX):

Body Mass Index is a height / weight formula used by health and weight professionals around the world to asses a person’s body weight, measuring the level of body fatness in an individual. From your body mass index number you can see if you are underweight, normal weight, overweight or obese

| THE RESULT | THE VALUE OF BMI |
| --- | --- |
| Underweight | Under 20 (19 for women) |
| Normal Weight | Between 20 and 24.99 |
| Overweight | Between 25 and 29.99 |
| Obese 1 | Between 30 and 34.99 |
| Obese 2 | Between 35 and 39.99 |
| Extreme Obesity | 40 and above |

- BMR (BASAL METABOLIC RATE):

Basal Metabolic Rate is the rate at which the body burns calories to maintain normal body functions while at rest. BMR is the largest factor in determining overall metabolic rate and how many calories you need to maintain, lose or gain weight.

To lose weight, you should try to eat fewer calories than your basic calories need. In order to lose weight, calories should not be your only concern. Exercise is vital, too.

- BODY FAT%:

You body fat percentage is simply the percentage of fat your body contains. If you are 150 pounds and 10% fat, it means that your body consists of 15 pounds fat and 135 pounds lean body mass, such as bone, muscle, organ tissue, blood and everything else.

“CONSOLE INSTRUCTIONS – BODY FAT PROGRAM (P8)”

“D. THE BODY FAT RESULT INFORMATION”

- BODY TYPE:

Refer to the following list to determine what your body type is:

| Type 1 | 5% ~ 9% (fat %) | Underweight | Type 2 | 10% ~ 14% (fat %) | Slim Class 1 |
| --- | --- | --- | --- | --- | --- |
| Type 3 | 15% ~ 19% (fat %) | Slim Class 2 | Type 4 | 20% ~ 24% (fat %) | Slim Class 3 |
| Type 5 | 25% ~ 29% (fat %) | Standard | Type 6 | 30% ~ 34% (fat %) | Overweight |
| Type 7 | 35% ~ 39% (fat %) | Obese Class 1 | Type 8 | 40% ~ 44% (fat %) | Obese Class 2 |
| Type 9 | 45% ~ 50% (fat %) | Extreme Obesity |  |

- ERROR INFORMATION:

If you do not place your hands on the Pulse Sensors correctly, the Pulse Sensors won’t be able pick up the signals. The console would then display an error message “E3”. To test it again, be sure to place your hands back on the Pulse Sensors correctly

“CONSOLE INSTRUCTIONS – H. R. C. PROGRAM (P9 ~ P12)”

“1” Prior information: Press any button on the console or begin pedaling to turn on the console

- Make sure that the power cord is properly plugged into the socket

- The console would automatically shut off after 4 minutes of inactivity

- Press any button on the console or begin pedaling to turn on the console. After a few seconds, the console will then light up with a short beep sound, indicating the console will be ready for use

“2” Prior information: ”HOLD TO RESET” button, an easy way to reset and enter into POWER ON status

Continue pressing START/PAUSE a few seconds, all the date will reset to the initial value and the console will return to POWER ON status

“3” Normal way to operate H.R.C. PROGRAM (P9~P12)

“A.“ENTER H.R.C. PROGRAM (P9~P12)”

- START/PAUSE button:

If you have selected other program (P1 ~ P8 or P13 ~ P16), pressing START/PAUSE button to pause the current program

- UP or DOWN button:

Press UP or DOWN button to select H.R.C. PROGRAM (P9 ~ P12)

- ENTER button:

Press ENTER button to confirm and enter H.R.C. PROGRAM (P9 ~ P12)

“CONSOLE INSTRUCTIONS – H. R. C. PROGRAM (P9 ~ P12)”

“B. SET THE DESIRED TIME or DESIRED DISTANCE

To avoid the user to select TIME and DISTANCE in the same program to confuse the user couldn’t distinguish which one (TIME or DISTANCE) as the first priority. User could only select TIME or DISTANCE in the same program, one at the time

| If you would like to select TIME value, not DISTANCE value: UP or DOWN button: After pressing the ENTER button to enter into H.R.C. PROGRAM (P9 ~ P12), the TIME function mode will appear with the display flashing “0:00” Use UP or DOWN buttons to set the desired TIME (1:00 TO 99:00; 1 MINUTE INCREMENT) NOTE for TIME: Count Up: If a target time was not selected, TIME will count up from 0:00 to maximum 99:59 minutes Count Down: If you have set the target time, the console will count down from that selected target time down to 0:00 | If you would like to select DISTANCE value, not TIME value: ENTER button and then UP or DOWN button: After pressing the ENTER button to enter into H.R.C. PROGRAM (P9 ~ 12), the TIME function mode will appear with the display flashing “0:00”. Press the ENTER button again, the DISTANCE function mode will then appear with the display flashing “0.0” Use UP or DOWN buttons to set the desired DISTANCE (1 TO 999KM/MILE; 1 KM/MILE INCREMENT) NOTE for DISTANCE: Count Up: If a target distance was not selected, this would measure the total distance from 0:00 to 999 km/mile Count Down: If you have set the target distance, the console will count down from the selected target time down to 0 |
| --- | --- |

“C. SET THE DESIRED CALORIES”

ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm the TIME or DISTANCE value and enter the mode to set the

CALORIES

b. Use UP or DOWN buttons to set the desired CALORIES (10 TO 9990KCAL; 10 KCAL

INCREMENT)

NOTE for CALORIES:

- Count Up: If target calories was not selected, this would measure total calories burned during exercise

- Count Down: If you have set the preference value of calories, the console will count down from that selected value down to 0

“CONSOLE INSTRUCTIONS – H. R. C. PROGRAM (P9 ~ P12)”

“D. SET THE TARGET HEART RATE or YOUR AGE”

| If you have selected PROGRAM 9, select TARGET HEART RATE: ENTER button and then UP or DOWN button: Press ENTER button to confirm the CALORIES value and enter the mode to set the TARGET H.R. Use UP or DOWN buttons to set the desired TARGET H.R. (60 ~ 220 BPM (BEATS PER MINUTE) ; 1 BPM INCREMENT) | If you have selected PROGRAM 10~12, select your AGE: ENTER button and then UP or DOWN button: Press ENTER button to confirm the CALORIES value and enter the mode to set the AGE Use UP or DOWN buttons to set your AGE (10 TO 99 YEARS OLD; 1 YEAR OLD INCREMENT) NOTE for AGE: NOTE: Although the console allows input for ages beginning at 10 years old, the product is not recommended for children’s use |
| --- | --- |

“ E. MUST-KNOWN HEART RATE PROGRAM INFO.”

  - SIMPLE FORMULA OVERVIEW:

BEGINNER: 60% of maximum heart rate; 60% of (220 – you age)

TRAINER: 75% of maximum heart rate; 75% of (220 – you age)

ACTIVE TRAINER: 85% of maximum heart rate; 85% of (220 – you age)

  - CONSOLE MONITOR YOUR CURRENT PULSE

    - The console will monitor your actual pulse and adjust the resistance/torque level automatically to keep your pulse within your TARGET HEART RATE ZONE.

    - If you current pulse > (the value of the TARGET HEART RATE ± 5), the console would decrease one resistance/torque level automatically

    - If you current pulse < (the value of the TARGET HEART RATE± 5), the console would increase one resistance/torque level automatically

For example: if your age is 30, 60% of your max. heart rate is 114. To determine your HEART RATE ZONE, the minimum number in your zone is 109 (114 – 5) and your maximum number in your zone is 119 (114 ( 5), so you TARGET HEART RATE ZONE in this example is 109 to 119. The program will monitor your pulse and adjust the torque/resistance level automatically to keep your pulse within the HEART RATE ZONE (109 – 119) during workout

“CONSOLE INSTRUCTIONS – H. R. C. PROGRAM (P9 ~ P12)”

“F. START EXERCISE”

START/ PAUSE button: Press START/ PAUSE to begin exercise. “START” would then appear on the screen

“ G. DURING WORKOUT, ALWAYS MONITOR YOUR CURRENT HEART RATE STATUS”

NOTE for HEART RATE:

- You must place both of your hands on the Pulse Sensors located on the Seat Handlebar. Your pulse will be displayed approximately few seconds after the heart symbol “” is             displayed

- If you do not place your hands correctly and a few seconds pass without a pulse input, the console will turn off the pulse circuit. The console will then display an error message

“P”. Place your hands back on the Pulse Sensors correctly, the pulse readout will appear again

“H. DURING WORKOUT, THE TORQUE/TENSION LEVEL IS EASILY CHANGED AT ANY TIME”

UP or DOWN button: You can change the torque/tension level (from 1 to 16 levels) at any time

during workout by pressing UP or DOWN button

I. DURING WORKOUT, HOW TO REVIEW SPEED, DISTANCE, CALORIES, RPM, ODO (ODOMETER) AND WATT”

During workout (after pressing START/PAUSE), the user could press MODE to select SPEED, DISTANCE and CALORIES, or RPM, ODO (Odometer) and WATT

RPM, ODO, WATT will show at the same time   SPEED, DISTANCE, CAL. will show at the same time

About ODO (odometer), the function is similar to DISTANCE, will accumulate the total distance traveled by the item during workout. If there is any necessary to reset ODO’s distance value, press UP, MODE, DOWN and ENTER at the same time to let the motor automatically calibrate to reset ODO value to zero

“CONSOLE INSTRUCTIONS – USER SETTING PROGRAM (P13 ~ P16)”

“1” Prior information: Press any button on the console or begin pedaling to turn on the console

- Make sure that the power cord is properly plugged into the socket

- The console would automatically shut off after 4 minutes of inactivity

- Press any button on the console or begin pedaling to turn on the console. After a few seconds, the console will then light up with a short beep sound, indicating the console will be ready for use

“2” Prior information: ”HOLD TO RESET” button, an easy way to reset and enter into POWER ON status

Continue pressing START/PAUSE a few seconds, all the date will reset to the initial value and the console will return to POWER ON status

“3” Normal way to operate USER MODE PROGRAM (P13~P16)

“A.“ENTER USER MODE PROGRAM (P13~P16)”

- START/PAUSE button:

If you have selected other program (P1 ~ P12), pressing START/PAUSE button to pause the current program

- UP or DOWN button:

Press UP or DOWN button to select USER MODE PROGRAM (P13 ~ P16)

- ENTER button:

Press ENTER button to confirm and enter USER MODE PROGRAM (P13 ~ P16)

“CONSOLE INSTRUCTIONS – USER SETTING PROGRAM (P13 ~ P16)”

“B. SET THE DESIRED TIME or DESIRED DISTANCE

To avoid the user to select TIME and DISTANCE in the same program to confuse the user couldn’t distinguish which one (TIME or DISTANCE) as the first priority. User could only select TIME or DISTANCE in the same program, one at the time

| If you would like to select TIME value, not DISTANCE value: UP or DOWN button: After pressing the ENTER button to enter into USER MODE PROGRAM (P13 ~ P16), the TIME function mode will appear with the display flashing “0:00” Use UP or DOWN buttons to set the desired TIME (1:00 TO 99:00; 1 MINUTE INCREMENT) NOTE for TIME: Count Up: If a target time was not selected, TIME will count up from 0:00 to maximum 99:59 minutes Count Down: If you have set the target time, the console will count down from that selected target time down to 0:00 | If you would like to select DISTANCE value, not TIME value: ENTER button and then UP or DOWN button: After pressing the ENTER button to enter into USER MODE PROGRAM (P13 ~ P16), the TIME function mode will appear with the display flashing “0:00” Press the ENTER button again, the DISTANCE function mode will then appear with the display flashing “0.0” Use UP or DOWN buttons to set the desired DISTANCE (1 TO 999KM/MILE; 1 KM/MILE INCREMENT) NOTE for DISTANCE: Count Up: If a target distance was not selected, this would measure the total distance from 0:00 to 999 km/mile Count Down: If you have set the target distance, the console will count down from the selected target time down to 0 |
| --- | --- |

“C. SET THE DESIRED CALORIES and YOUR AGE”

ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm TIME or DISTANCE value and enter the mode to set the

CALORIES

b. Use UP or DOWN buttons to set the desired CALORIES (10 TO 9990KCAL; 10 KCAL

INCREMENT)

NOTE for CALORIES:

- Count Up: If target calories was not selected, this would measure total calories burned during exercise

- Count Down: If you have set the preference value of calories, the console will count down from that selected value down to 0

“CONSOLE INSTRUCTIONS – USER SETTING PROGRAM (P13 ~ P16)”

“D. SET THE DESIRED CALORIES and YOUR AGE”

ENTER button and then UP or DOWN button:

a. Press ENTER button to confirm the CALORIES value and enter the mode to set the AGE

b. Use UP or DOWN buttons to set your AGE (10 TO 99 YEARS OLD; 1 YEAR OLD INCREMENT)

NOTE for CALORIES:

NOTE: Although the console allows input for ages beginning at 10 years old, the product is not recommended for children’s use

“E. SET THE TORQUE/RESISTANCE LEVEL”

ENTER button and then UP or DOWN button:

- The USER SETTING PROGRAM allows the user to manually set the torque/resistance level, the console will divide the time into 10 intervals. The user could through their preference to set the desired torque/resistance level in each time interval

- Press ENTER button to confirm the AGE value and enter the mode to set the EACH TIME INTERVAL OF TORQUE/RESISTANCE LEVEL (1 TO 16 TORQUE/RESISTANCE LEVELS; 1 TORQUE/RESISTANCE LEVEL INCREMENT), then press ENTER button to confirm

- Continue following the above process to finish setting the preference

TORQUE/RESISTANCE LEVEL in 10 time intervals. The program profile will be storied in the memory after setup. You can modify the profile anytime under the STOP mode

“F. START EXERCISE”

START/ PAUSE button: Press START/ PAUSE to begin exercise. “START” would then appear to the screen

“ G. DURING WORKOUT, ALWAYS MONITOR YOUR CURRENT HEART RATE STATUS”

NOTE for HEART RATE:

- You must place both of your hands on the Pulse Sensors located on the Seat Handlebar. Your pulse will be displayed approximately few seconds after the heart symbol “” is displayed

- If you do not place your hands correctly and a few seconds pass without a pulse input,

the console will turn off the pulse circuit. The console will then display an error message “P”. Place your hands back on the Pulse Sensors correctly, the pulse readout will appear again.

“CONSOLE INSTRUCTIONS – USER SETTING PROGRAM (P13 ~ P16)”

“H. DURING WORKOUT, THE TORQUE/TENSION LEVEL IS EASILY CHANGED AT ANY TIME”

UP or DOWN button: You can change the torque/tension level (from 1 to 16 levels) at any

time during workout by pressing UP or DOWN button

I. DURING WORKOUT, ALWAYS NOTICE TARGET HEART RATE – A EASY WAY TO SET A GOAL TO “STRENGTHEN YOUR CARDIOVASCULAR WORKOUT”

- To improve your cardiovascular condition, while input your personal age during the setting mode, the console will calculate the appropriate TARGET HEART RATE for you automatically

- The TARGET HEART RATE calculation is based on 85% of the maximum heart rate. For example: For a 30-year-old user, the max. user heart rate should be 161 = (220-30) x 85%

- The console will monitor your pulse and compare the value of your pulse with TARGET HEART RATE. The value of HEART RATE will keep flashing to warn you to slow down or lower the torque/resistance level if your pulse value is greater than TARGET HEART RATE

J. DURING WORKOUT, HOW TO REVIEW SPEED, DISTANCE, CALORIES, RPM, ODO (ODOMETER) AND WATT”

During workout (after pressing START/PAUSE), the user could press MODE to select SPEED, DISTANCE and CALORIES, or RPM, ODO (Odometer) and WATT

RPM, ODO, WATT will show at the same time   SPEED, DISTANCE, CAL. will show at the same time

About ODO (odometer), the function is similar to DISTANCE, will accumulate the total distance traveled by the item during workout. If there is any necessary to reset ODO’s distance value, press UP, MODE, DOWN and ENTER at the same time to let the motor automatically calibrate to reset ODO value to zero

“CONSOLE TROUBLE SHOOTING GUIDE“

| PROBLEM | POSSIBLE CAUSE | SOLUTION |  |
| --- | --- | --- | --- |
| E1 | No Motor signal | 1. Motor Malfunction | Replace Motor |
|  |  | 2. Magnetic System Malfunction or got stuck | Replace Magnetic System/Flywheel |
|  |  | 3. Connection Wires are not well-connected or broken | Check whether the wires are well-connected or replace the broke wires with the new wires |
|  |  | 4. Console Malfunction | Replace Console |
| E2 | The Computer cannot make contact with the IC Chip | 1. Disconnect the Adaptor or Batteries. Reconnect the Adaptor or Batteries to REBOOT the system. Wait two minutes then verify that the system works correctly |
|  |  | 2. If IC Chips is not well-assembled. Remove and reinsert the IC Chip |
|  |  | 3. If the above solutions couldn’t solve the problem, replace the IC chip with a New IC Chip |
| E3 | No heart rate signal after Body Fat testing result when in Body Fat Program (P8) | If you do not place your hands on the Pulse Sensors correctly, the Pulse Sensors won’t be able pick up the signals. The console would then display an error message “E3”. To test it again, be sure to place your hands back on the Pulse Sensors correctly |
| E5 | Motor couldn’t return to the initial setup value/zero point | 1. Check whether the wires are broken or well-connected | Replace the broken wires with new wires or re-connected the wires |
|  |  | 2. Check whether the motor is broken (has struggle to adjust the resistance and will make an abnormal noise) | Replace Motor |
|  |  |  | Replace Magnetic System |
| No Hand Pulse Signal or incorrect Hand Pulse Signal | The Computer is NOT receiving a Pulse Signal | Verify that the Hand Pulse Sensor Wire Plugs are connected FIRMLY and correctly |
|  | The Computer is receiving a faint or intermittent Pulse Signal | The Hand Pulse Sensors will NOT operate correctly if your skin is extremely dry. Moisten your hands with a little water and try again. |
|  |  | Grasp the Hand Pulse Sensors firmly and avoid moving your hands while exercising. The computer will need a few seconds to detect and display your correct pulse rate. If this does not work, try relaxing your grip on the Hand Pulse Sensors |
|  |  | Clean the Hand Pulse Sensors to ensure a good contact between your body and the Pulse Sensors |
|  |  | The problem still exists, replace the Hand Pulse Sensors. |
| The LCD Screen does not display anything | The Adaptor is not plugged in (item power supply from Adaptor) | Check that the Adaptor is correctly connected to an electrical outlet and plugged into the socket on the machine correctly |
|  | The Computer is faulty | Replace the Computer |

“CONSOLE TROUBLE SHOOTING GUIDE“

| PROBLEM | POSSIBLE CAUSE | SOLUTION |
| --- | --- | --- |
| The Speed Display Show “O” | The Computer isn’t receiving a signal from the Speed Sensor? | Verify the gap between Speed Sensor and the Magnet is 5mm or less |
|  |  | Verify that all the Wire Plugs are connected FIRMLY, correctly and are not damaged |
|  |  | Verify that the sensor Magnet is installed correctly |
|  | The Sensor is faulty | Replace the Speed Sensor |
|  | The Computer is faulty | Replace the Computer |
| The LCD Screen Partially Displays | The connection between the Circuit Board and the LCD Membrane is loose. Gently press down on the LCD Screen, if the partial display disappears, then it is a connection problem | Verify that the Circuit Board is securely fastened to the Computer Case. Retighten the Screws. Take care NOT to over tighten the Screws as this may destroy the Circuit Board. You just need to keep the Circuit Board firm, STOP tightening screw when you meet resistance |
|  | The Rubber Membranes between the Circuit Board and the LCD Screen is misaligned/not in a same line. You might be able to see that the LCD Screen is on a slight angle and NOT inline or parallel with the Console Cover | Open the Console. Remove the Circuit Board’s Screws, gently remove the Circuit Board, Re-align the LCD screen and the Rubber Membrane. Reassemble the Circuit Board and taking care not to bump or knock the Rubber Membrane out of alignment before the Circuit Board Screws are tight. You just need to keep the Circuit Board firm, STOP tightening screws when you meet resistance |
|  | The Computer is faulty | Replace the Computer |

“CONDITIONING GUIDELINES”

How you begin your exercise program depends on your physical condition. If you have been inactive for several years, or are severely overweight, you must slowly and increase your time on the item gradually: a few minutes per workout.

Initially, you may be able to exercise only for a few minutes in your target zone, however, your aerobic fitness will improve over the next six to eight weeks. Don’t be discouraged if it takes longer. It’s important to work at your own pace. Ultimately, you’ll be able to exercise continuously for 30 minutes. The better your aerobic fitness, the harder you will have to work to stay in your target zone. Please remember these essentials:

˙ Have your doctor review your training and diet programs to advise you of a workout routine you should adopt.

˙ Begin your training program slowly with realistic goals that have been set by you and your doctor.

˙ Monitor your pulse frequently. Establish your target heart rate base on your age and condition.

˙ Set up your 2 in 1 Elliptical / Stepper a flat, even surface at least 3 feet from walls and furniture.

EXERCISE INTENSITY

To maximize the benefits of exercising, it is important to exercise with the proper intensity. The proper intensity level can be found by using your heart rate as a guide. For effective aerobic exercise, your heart rate should be maintained at a level between 70% and 85% of your maximum heart rate as you exercise. This is known as your target zone. You can find your target zone in the table below. Target zones are listed for both unconditioned and conditioned persons according to age.

During the first few months of your exercise program, keep your heart rate near the low end of your target zone as you exercise. After a few months, your heart rate can be increased gradually until it is near the middle of your target zone as you exercise.

To measure your heart rate manually, stop exercising but continue moving your legs or walking around and place two fingers on your wrist. Take a six-second heartbeat count and multiply the results by 10 to find your heart rate. For example, if your six-second heartbeat count is 14, your heart rate is 140 beats per minute. (A six-second count is used because your heart rate will drop rapidly when you stop exercising.) Adjust the intensity of your exercise until your heart rate is at the proper level.

“WARM-UP AND COOL-DOWN”

Warm-up The purpose of warming up is to prepare your body for exercise and to minimize injuries. Warm up for two to five minutes before strength-training or aerobic exercising. Perform activities that raise your heart rate and warm the working muscles. Activities may include brisk walking, jogging, jumping jacks, jump rope, and running in place.

Stretching Stretching while your muscles are warm after a proper warm-up and again after your strength or aerobic training session is very important. Muscles stretch more easily at these times because of their elevated temperature, which greatly reduces the risk of injury. Stretches should be held for 15 to 30 seconds. Do not bounce.

Suggested Stretching Exercises

|  | Lower Body Stretch Place feet shoulder-width apart and lean forward. Keep this position for 30 seconds using the body as a natural weight to stretch the backs of the legs. DO NOT BOUNCE! When the pull on the back of the legs lessen, try a lower position gradually. |  | Floor Stretch While sitting on the floor, open the legs as wide as possible. Stretch the upper body toward the knee on the right leg by using your arms to pull your chest to your thighs. Hold this stretch 10 to 30 seconds. DO NOT BOUNCE! Do this stretch 10 times. Repeat the stretch with the left leg. |
| --- | --- | --- | --- |
|  | Bent Torso Pulls While sitting on the floor, have legs apart one leg straight and one knee bent. Pull the chest down to touch the thigh on the leg that is bent and twist at the waist. Hold this position at least 10 seconds. Repeat 10 times on each side. |  | Bent Over Leg Stretch Stand with feet shoulder-width apart and lean forward as illustrated. Using the arms, gently pull the upper body towards the right leg. Let the head hand down. DO NOT BOUNCE! Hold the position a minimum of 10 seconds. Repeat pulling the upper body to the left leg. Do this stretch several times slowly. |

Remember always to check with your physician before starting any exercise program.

Cool-Down The purpose of cooling down is to return the body to its normal, or near normal, resting state at the end of each exercise session. A proper cool-down lowers your heart rate and allows blood to return to the heart. Your cool-down should include the stretches listed above and should be completed after each strength-training session.

“PRODUCT PARTS DRAWING (A)”

“PRODUCT PARTS DRAWING (B)”

“PART LIST”

| NO. | Part Name | Q'ty |
| --- | --- | --- |
| 1 | Main Frame | 1 |
| 2 | Front Stabilizer | 1 |
| 3 | Rear Stabilizer | 1 |
| 4 | Left Sliding Rail | 1 |
| 5 | Right Sliding Rail | 1 |
| 6 | Upright Post | 1 |
| 7 | Fixed Handlebar | 1 |
| 8 | Left Upper Handlebar | 1 |
| 9 | Right Upper Handlebar | 1 |
| 10 | Left Middle Handlebar | 1 |
| 11 | Right Middle Handlebar | 1 |
| 12 | Pivoting Arm | 2 |
| 13 | Left Pedal Support Arm | 1 |
| 14 | Right Pedal Support Arm | 1 |
| 15 | Linkage | 2 |
| 16 | Pedal Arm Connector | 2 |
| 17 | Left Chain Cover | 1 |
| 18 | Right Chain Cover | 1 |
| 19 | Crank Cover | 2 |
| 20 | Pulley | 1 |
| 21 | Magnet | 1 |
| 22 | Belt (1168 J6) | 1 |
| 23 | Leveler | 1 |
| 24 | Tube Decoration Cover for Stabilizer | 1 |
| 25 | Transportation Wheel | 2 |
| 26 | EndCap | 2 |
| 27 | Adjusting Rear Stabilizer EndCap | 2 |
| 28 | Bushing | 4 |
| 29 | Bushing (flat) | 4 |
| 30 | Securing Cap (38.1mm) | 4 |
| 31 | Rail Sleeve | 2 |
| 32 | Console | 1 |
| 33 | Console Bottom Cover | 1 |
| 34 | Left Console Sleeve | 1 |
| 35 | Right Console Sleeve | 1 |
| NO. | Part Name | Q'ty |
| 36 | Rotator Cuff | 2 |
| 37 | Upright Sleeve | 1 |
| 38 | Hand Pulse Upper Cover | 2 |
| 39 | Hand Pulse Bottom Cover | 2 |
| 40 | Handlebar Decoration Cover | 2 |
| 41 | Round Plug | 2 |
| 42 | Foam Grip for Upper Handlebar | 2 |
| 43 | Handheld Plug | 2 |
| 44 | Handlebar Sleeve | 2 |
| 45 | Middle Handlebar Bushing | 4 |
| 46 | Securing Cap (ψ60) | 2 |
| 47 | Round Plug (25.4mm) | 2 |
| 48 | Spring Knob | 2 |
| 50 | Bushing (12×38mm) | 4 |
| 51 | Round Plug (38.1mm) | 2 |
| 52 | Square Plug (25.4mm) | 4 |
| 53 | Non-Slip Pad | 6 |
| 54 | Pedal Upper Case | 2 |
| 55 | Sliding Roller | 2 |
| 56 | Roller Spacer | 2 |
| 57 | Bushing (17×33.4mm) | 4 |
| 58 | Linkage Plug | 2 |
| 59 | Left Upright Post Cover | 1 |
| 60 | Right Upright Post Cover | 1 |
| 61 | Pulse Sensor Housing w/ Sensor Plate | 4 |
| 62 | Flywheel | 1 |
| 63 | Axle | 1 |
| 64 | Left Crank | 1 |
| 65 | Right Crank | 1 |
| 66 | Fixed Plate for Motor | 1 |
| 67 | Cable | 1 |
| 68 | Shaft Sleeve | 2 |
| 69 | Roller Bracket | 4 |
| 70 | Bearing (6000) | 4 |
| 71 | Bearing (6004) | 2 |

“PART LIST”

| NO. | Part Name | Q'ty |
| --- | --- | --- |
| 72 | Bearing (6300) | 2 |
| 73 | Spacer (10×14×2mm) | 2 |
| 74 | C-Ring | 1 |
| 75 | E-Ring | 2 |
| 76 | Eye Bolt | 2 |
| 77 | Tension Bracket | 2 |
| 78 | Wave Washer | 1 |
| 79 | Lock Washer | 15 |
| 80 | Washer (8×16×2.0t) | 11 |
| 81 | Washer (8×60×2.0t) | 2 |
| 82 | Washer (10×23×2.0t) | 10 |
| 83 | Washer (17×33.4×0.5t) | 4 |
| 84 | Washer (21×30×0.5t) | 2 |
| 85 | Washer (21×30×1.0t) | 1 |
| 86 | Screw (M3×25mm) | 4 |
| 87 | Screw (M4×16mm) | 4 |
| 88 | Screw (M4×16mm) | 7 |
| 89 | Bolt (M5×18mm) | 17 |
| 90 | Bolt (M5×p0.8×25mm) | 4 |
| 91 | Bolt (M5×p0.8×15mm) | 4 |
| 92 | Bolt (M5×p0.8×25mm) | 2 |
| 93 | Bolt (M6×p1.0×25mm) | 12 |
| 94 | Bolt (M8×p1.25×16mm) | 4 |
| 95 | Bolt (M5×p0.8×12mm) | 4 |
| 96 | Bolt (M8×p1.25×15mm) | 2 |
| 97 | Bolt (M5×p0.8×15mm) | 2 |
| 98 | Bolt (M6×p1.0×15mm) | 4 |
| 99 | Bolt (M6×p1.0×35mm) | 4 |
| 100 | Bolt (M8×p1.25×45mm) | 1 |
| 101 | Bolt (M8×p1.25×90mm) | 2 |
| 102 | Bolt (M8×p1.25×16mm) | 4 |
| NO. | Part Name | Q'ty |
| 103 | Bolt (M8×p1.25×20mm) | 4 |
| 104 | Bolt (M8×p1.25×50mm) | 2 |
| 105 | Bolt (M8×p1.25×65mm) | 2 |
| 106 | Bolt (M8×p1.25×90mm) | 2 |
| 107 | Bolt (M10×p1.5×85mm) | 2 |
| 108 | Bolt (M8×p1.25×16mm) | 4 |
| 109 | Carriage Bolt (M8×p1.25×90mm) | 2 |
| 110 | Nylon Nut (M6×p1.0) | 6 |
| 111 | Thin Nylon Nut (M8×p1.25) | 4 |
| 112 | Nylon Nut (M8×p1.25) | 13 |
| 113 | Nylon Nut (M10×p1.5) | 3 |
| 114 | Nut (M8×p1.25) | 1 |
| 115 | Flange Nut (M10) | 2 |
| 116 | Flange Nut - Black Color (M10) | 2 |
| 117 | Upper Connection Wire | 1 |
| 118 | Middle Connection Wire | 1 |
| 119 | Lower Connection Wire | 1 |
| 120 | Sensor Wire & Stand | 1 |
| 121 | Motor | 1 |
| 122 | Adaptor Connection Wire | 1 |
| 123 | Adaptor | 1 |
| 124 | Upper Pulse Sensor Wire | 1 |
| 125 | Lower Pulse Sensor Wire | 1 |
| 126 | Middle Handlebar Connection Plug | 2 |
| 127 | Pivoting Arm Connection Plug | 2 |
| 128 | Left Handrail Base Cover | 2 |
| 129 | Right Handrail Base Cover | 2 |
| 130 | Pedal Bottom Case | 2 |
| 131 | Screw (M4×10mm) | 6 |

# Text boxes

Product May Vary Slightly From Picture MADE IN TAIWAN

Exercise can present a health risk. Consult a physician before beginning any exercise program with this equipment.

If you feel faint or dizzy, immediately discontinue use of this equipment. Serious bodily injury can occur if this equipment is not assembled and used correctly. Serious bodily injury can also occur if all instructions are not followed.

Keep children and pets away from equipment when in use. Always make sure all bolts and nuts are tightened prior to each use. Follow all safety instructions in this manual.

CAUTION: WEIGHT ON THIS PRODUCT SHOULD NOT EXCEED 136KG / 300LBS.

OWNER’S

MANUAL

Console

Upper Handlebar

Hand Pulse Sensor

Main Frame

Pedal

Spring Knob

Pedal Rail

Sliding Roller

Adjustable Rear Stabilizer EndCap

ALLEN WRENCH

(5 mm)

PHILLIPS

SCREWDRIVER (6mm)

WRENCH

(10 & 13 mm)

For letting the sliding rail assembly attaches nicely to the rear stabilizer, please don’t fully tighten on Step 2

NOTE: “Small Tip: Attach screws and bolts to the assembly parts first before secure”

To assemble the Front Stabilizer (2) to the Maine Frame (1) with more efficient and easy way, it is suggested to attach two Washers (8x16x2.0t)(80), two Lock Washers (M8)(79) and two Bolts (M8xp1.25x90mm)(101) to the Front Stabilizer (2) and the Maine Frame (1) first before fully secure. **Please do not secure the bolts unless you make sure Bolts all go into screw holes of Front Stabilizer and Main Frame**

- Take a few minutes to review the console layout. Below is an overview of the console’s features and functions

- We recommend that you use the console to help vary your workout routine and keep you focused on your process toward your fitness goals. The console can become an important source of motivation and interest which will help keep you on track

POWER ON status

- START/PAUSE button:

If you have selected other program (P2~P16), pressing START/PAUSE button to pause the current program

- UP or DOWN button:

Press UP or DOWN button to select MANUAL PROGRAM (P1)

- ENTER button:

Press ENTER button to confirm and enter MANUAL PROGRAM (P1)

ENTER button:

When the power is turned on, the manual program (P1) will be selected, pressing ENTER button to confirm and enter MANUAL PROGRAM (P1)

or

POWER ON status

POWER ON status

The illustration on the left is just an example to show you what the result should look like, each person has different body fat condition depends on the user’s current health condition from time to time

BMI conclusion very slightly according to gender. Here is a general summary of weight-status based on BMI

60% H.R.C.

T.H.R.

85% H.R.C.

75% H.R.C.

POWER ON status

FIND YOUR TARGET HEART RATE

POWER ON status

| Age | Target Heart Rate Zone (55% ~ 90% of Max. Heart Rate) | Average Max. Heart Rate 100% |
| --- | --- | --- |
| 20 | 110-180 beats per minute | 200 beats per minute |
| 25 | 107-175 beats per minute | 195 beats per minute |
| 30 | 105-171 beats per minute | 190 beats per minute |
| 35 | 102-166 beats per minute | 185 beats per minute |
| 40 | 99-162 beats per minute | 180 beats per minute |
| 45 | 97-157 beats per minute | 175 beats per minute |
| 50 | 94-153 beats per minute | 170 beats per minute |
| 55 | 91-148 beats per minute | 165 beats per minute |
| 60 | 88-144 beats per minute | 160 beats per minute |
| 65 | 85-139 beats per minute | 155 beats per minute |
| 70 | 83-135 beats per minute | 150 beats per minute |